11 SATA Interface

12 USB Interface
	OK	Wrong	Comments
Ensure that when working in host mode a 120uF capacitor is connected on the USB VBUS close to the connector.
Ensure that ISET_RES (same resistor for both SATA and USB), is pulled down by 6.04 kΩ resistor to VSS. The resistor accuracy must be ± 1%.
Ensure the implementation of the USB_AVDD filter conforms to the Design Guide:
Ensure to follow the VBUS connection method described in the Design Guide, an example reference for both host and device is in the figure bellow.
It is recommended to add an ESD/EMI protection circuit on USB_DP/USB_DM signals, as described bellow:
If this interface is unused, discard the power filter, leave USB_AVDD connected to 3.3V.

	OK	Wrong	Comments
Ensure there is a pull up resistor of 4. 7 kΩ to VDDO 3.3V on TDM_SPI_CSn
Ensure there is a pull up resistor of 4. 7 kΩ to VDDO 3.3V on TDM_INTn
Ensure there is a pull down resistor of 4. 7 kΩ to GND on TDM_Resetn
Ensure that when working in daisy chain mode there is up to 8 devices on the TDM_SPI interface