Outline
- The diode
  - Special diodes
  - Diode applications

---
Diode
Zener diodes
- Diodes where the “Zener” effect is dominant in the reverse breakdown
  - Phenomenon can be very accurately characterized
  - Diodes can be designed to have different “Zener voltages”
    - Zener voltage is only slightly dependent on temperature
    - A Zener diode in Zener breakdown behaves as an ideal voltage source
    - Used as a voltage reference
      - Always use a series resistance as a current limiting means

---
Light emitting diodes
- Special diodes that emit light when forward biased and conducting current
  - Called “LEDs”
  - Light is emitted because photons are produced when electrons and holes can recombine
  - The energy gap determines the energy of the photon and thus the color of the light
    - Light is generally monochromatic

---
Light emitting diodes	(2)
- LEDs are often used for signaling and to build displays
  - They behave as diodes, but they have a much larger threshold voltage (e.g., 1.5 ÷ 2 V)
  - Data sheet needs to be checked for threshold voltage and current necessary to produce the desired amount of light (typically 20 ÷ 25 mA)
  - A current limiting mechanism (typically a resistor) is always required when using LEDs

---
Light emitting diodes	(3)
Combining many LEDs, one can build displays too!

---
Light emitting diodes	(4)
Sample circuit with a LED that is directly driven by an OPAMP.
Led is in “common anode” configuration and lights up when the OPAMP output goes low.
Circuit reports when a cursor (linked to the potentiometer) moves beyond a certain point by lighting the LED
Note the resistor that is necessary to limit the current on the LED!